4.The way for selecting the FDK 0.15-5KW wind-power generator controller fitting the

FDM 0.15-5KW

# Text boxes

VM

FDK0.15-50KW Wind-Power Generator System Controller

1. Description and Usage:

This FDK 0.15-50KW wind-power generator system controller is the effective control device and it is the necessary accessory to the generator system. It is the combination of the electric battery, the cabinet and the reverse-exchange device of electric circuit with the function of automatic rectification charge and automatic protection. It can be used to charge A/C generated by the wind-power generator to D/C for charging the battery and to supply the reverse the electricity for transmitting the electricity for the outdoor usage. There are two constructive forms of this system subject to the different installation places: One is of high protection class system installed beneath the pole of the generator. It is mainly for producing the power of 1KW and below. And the another form is installed in the room. The out-put voltage can be selected by the user.

A

B

C/C1

D

General idea for the selection of the system: Normally people have to consider the following facts when they are going to select the generator system: Power, Voltage, Price, Wind-force and the Installation Position of the wind-power generator (M8). Some facts can be consulted with the local electric engineers.
  The selection of the power generated by the generator is subject to the consumable power ( Normally the former should be 30% bigger than the latter). For example, if the consumable power is 750W, the power generated (M8) should be 1KW. The out-put voltage of system controller ( M1,M2,M3 ) is selective of DC 24V, 48V or AC 110V, 220V, 380V and 440V. The battery group is designed on the standard of 5-8 hours' usage per day. Some special design will be required if longer usage time is needed. M7 is the solar energy board for the customer's selection: Controller of M1 and M2 of 1KW or below can be installed both indoor or outdoor. This system can be operated both with the electric net or independently.
More detai linformation will be available on the customers' requirement.

Brief Introduction

M1

MUCE

M2

M3

2.Main Feature and Technical Specification:
Power: 0.15-50KW,
Input Voltage: 48V-400V,
Output Voltage: 48V DC, 220V DC and 38V DC
LCD Show: Voltage, Current and Charging and
Discharging Position,
Protection Function: Over-Voltage, Over-Current,
Short-Circuit, Over-Load and Alarming
Management Function: Time Showing, Magnetic Card and
Memory

3.Specification and Dimension:

Power      Combination            A    B      C/C1     D

FDK-0.15  150W   Cabinet/   520  420 200/360

FDK-0.3   300W    M1      520  420 200/360

FDK-0.5   500W  Cabinet/    520  420 200/360

FDK-1    1KW     M2      520  420 200/360

FDK-3    3KW    Cabinet/   520  420

FDK-10  10KW     M3      520  420        1500

FDK-50   50KW             620  420

wind-power generator system is:

M8

M7

3～5KW

M3  M6

M1

M2

4.The way for selecting the FDK 0.15-5KW wind-power generator controller fitting the FDM 0.15-5KW